## Slide 1: ASEN 5067 Final Project
William Watkins
ASEN 5067: Microavionics
13 December, 2021

## Slide 2: Project Overview: Media Control Center!
Goal was to implement media controls for future use on a keyboard
  To eliminate need to continuously switch back and forth between apps!
Levels of Success
  RPG changes Host PC volume
  Mute button mutes Host PC
  Play/pause button start/stops current track
  Next/previous buttons skip to next track/goes to previous track

## Slide 3: Hardware Overview
EasyPIC Pro board
  4 buttons on PORTD are used for Mute, Play/Pause, Next, and Previous
  RPG plugged into PORTD is used for volume control
  EUSART1 used to send data to the PC
SiliconLabs CP2110 Development Board
  Used as interface between PIC18 and PC
  Initializes as an Human Interface Device (HID) compatible device on plug in
  Translates serial data from EUSART1 to USB data

## Slide 4: Software Flow

## Slide 5: Achievements
No levels of success achieved
Even with multiple offramps used!
  SiliconLabs Serial-HID Chip/Board
  Using provided RPG
  Using EasyPIC Pro buttons instead of matrixed key array

## Slide 6: Obstacles and Lessons
Obstacles
  Implementing native USB communication
  Implementing native HID communication through “bit-banging”
  Implementing hardware!
Lessons
  Be slightly more cautious when leaping into a project
  Never trust when a forum post says “It’s easy”!
  Explore more than one offramp
  Be willing to pivot and change project if nothing is working!

## Slide 7: Future Work
Purchasing a PIC18F87J50
  Capable of native USB 2.0
  Eliminates need for Serial-HID board
  Order custom PCBs for use with mechanical keyboard switches and custom rotary encoder
  Implement matrix scan for whole keyboard